## Slide 1
Advanced Wastewater Treatment
University of Kansas
100th Annual Water and Wastewater School
Lawrence, Kansas
August 1, 2019
Grant Weaver, PE & wastewater operator
G.Weaver@CleanWaterOps.com

## Slide 2: Kansas Nutrient Reduction Strategy
total-Nitrogen total-Phosphorus
Mechanical Plants 10 mg/L 1.0 mg/L
Lagoons no increase no increase

## Slide 3: Wastewater treatment for Beginning Operators
Grow bacteria that feed on soluble pollutants
Settle out the bacteria
Send clean water into the stream

## Slide 4: Wastewater treatment for Advanced Operators
Grow bacteria that feed on soluble pollutants by maintaining optimal living conditions for the bacteria that treat wastewater
    BOD
    Nitrogen
    Phosphorus
    Alkalinity / pH

## Slide 5: Wastewater treatment for Advanced Operators
Grow bacteria that feed on soluble pollutants by maintaining optimal living conditions for the bacteria that treat wastewater
    BOD
    Nitrogen
    Phosphorus
    Alkalinity / pH
Settle out the bacteria by managing clarifiers and excellent process control

## Slide 6: Wastewater treatment for Advanced Operators
Grow bacteria that feed on soluble pollutants by maintaining optimal living conditions for the bacteria that treat wastewater
    BOD
    Nitrogen
    Phosphorus
    Alkalinity / pH
Settle out the bacteria by managing clarifiers and excellent process control
Send cleaner water into the stream

## Slide 7: Wastewater treatment for Advanced Operators
Grow bacteria that feed on soluble pollutants by maintaining optimal living conditions for the bacteria that treat wastewater
    BOD
    Nitrogen
    Phosphorus
    Alkalinity / pH
Settle out the bacteria by managing clarifiers and excellent process control
Send cleaner water into the stream
Create the right conditions to maximize the controlled release of nitrogen gas

## Slide 9: Advanced Wastewater Treatment
Process control!
Collect data
Compile, analyze, and interpret data
Intelligently apply data

## Slide 10: Process Control
Set Process Control targets; e.g., Aeration ORP and DO
Monitor for the right parameters in the right places
Record data on a Daily Log
Assign someone the responsibility for DAILY analyzing and using the data
Develop relationships; e.g., Aeration ORP vs. Ammonia Removal
Periodically, review and update procedures

## Slide 11: Process Control Targets
Conventional Treatment:
Aeration Basin DO / ORP
Aeration Basin MLSS / Sludge Age
Clarifier RAS, WAS, blanket depth
UV irradiance / transmittance
Nitrogen Removal:
Ammonia Removal
Aeration Basin DO / ORP (for phosphorus, too)
Aeration Basin Alkalinity / pH (for phosphorus, too)
Final effluent Ammonia
Nitrate Removal
Anoxic Zone ORP
Anoxic Zone Nitrate
Final effluent Nitrate
Phosphorus Removal:
Phosphorus Release
Fermenter ORP
Fermenter orthophosphate
Phosphorus Uptake
Aeration Basin DO / ORP and Alkalinity / pH
Final effluent orthophosphate

## Slide 12: Measurement Tools

## Slide 13: ORP or Oxidation Reduction Potential
Fermenter
Phosphorus Release
Aeration Basin
Ammonia Removal
Phosphorus Uptake
Anoxic Zone
Nitrate Removal

## Slide 15: Ammonia
Aeration Basin
Profile
Final Effluent
Daily performance

## Slide 16: Nitrate
Anoxic Zone
Daily performance
Final Effluent
Daily performance

## Slide 17: Phosphorus
Fermenter
Weekly performance
Aeration Basin
Weekly performance
Final Effluent
Daily performance

## Slide 18: Field testing for phosphorus
Phosphorus limits and commercial lab results report phosphorus – both total-phosphorus and orthophosphate – as P, phosphorus.
Many machines report orthophosphate “as PO4.”
If so, reset machine to record “as PO4-P” or, the same thing, “as P.”
If you can’t change the readings, divide “as PO4” results by 3 to get “as PO4-P” or “as P” values.

## Slide 19
Daily Log

## Slide 20
Put Process Control Data to Use
Establish targets for each test
ORP
Ammonia, Nitrate, Orthophosphate
Know what to do if readings are above or below targets
Fermenter
Aeration Basin
Anoxic Zone
Final Effluent
Refine and update targets
Seasonality
Changing Influent Characteristics

## Slide 21
Aero-Mod

## Slide 22
Aero-Mod
Fermenter / Selector
Anoxic Zone
Aerobic Zone
Clarifier
Clarifier
Aerobic Zone
Anoxic Zone

## Slide 23
Aero-Mod
Fermenter / Selector
Aerobic Zone
Anoxic Zone
Clarifier
Clarifier
Anoxic Zone
Aerobic Zone

## Slide 25
Sequencing Batch Reactor
SBR

## Slide 26
Air ON
Decant / Waste
Sequencing Batch Reactor (SBR)
Settle, Decant & Waste Sludge
Sludge Storage
SBR #1
SBR #2

## Slide 27
Idle
Air ON
Sequencing Batch Reactor (SBR)
Ammonia (NH4) Removal: Nitrification
Sludge Storage
NO3
NH4
SBR #1
SBR #2

## Slide 28
Idle
Air OFF
Sequencing Batch Reactor (SBR)
Nitrate (NO3) Removal: Denitrification
Sludge Storage
N2
NO3
SBR #1
SBR #2

## Slide 29
Oxidation Ditch

## Slide 31: Comments & Questions
Grant Weaver
g.weaver@cleanwaterops.com